## Slide 1: HKN ECE 310 Quiz 6 Review Session
Corey Snyder

## Slide 2: Topics
Digital Rate Conversion: Upsampling, Downsampling
D/A: Review of Ideal and ZOH, Upsampled D/A
FFT: Decimation in Frequency and Time
Circular Convolution, Linear Convolution using FFT

## Slide 3: Upsampling
If we upsample by L, we will interpolate L – 1 zeros between each sample
  if n mod L = 0
  0 else
What happens in the frequency domain?
  Think about what happens when we oversample and signal, i.e. above Nyquist?
What does the frequency response look like after upsampling?
  Shrink x-axis by factor of L
What should GD(ω) be in order to obtain a desirable frequency response?
  Remove extra copies and correct amplitude for conservation of energy

## Slide 4: Review: Ideal D/A
Want , but we want to only take one copy of the DTFT
  Thus, we should low-pass filter from (domain of the central copy of the DTFT)
Inverse CTFT of
Remember that multiplication in the frequency domain is convolution in the time domain
  Thus, , where is obtained by multiplying y[n] by an impulse train

## Slide 5: Review: Zero-Order Hold
Ideal D/A is not practical because generating delta impulses is not achievable
Zero-Order Hold (ZOH) gives us a suitable approximation to the Ideal D/A
The ZOH multiplies each sample by a rectangular pulse of width T (our sampling rate)
  Thus, where is the rectangular pulse provided by the ZOH
is an analog filter that corrects the distortion presented by the ZOH

## Slide 6: Upsampled D/A
Upsampling prior to D/A conversion can make recovery simpler
  i.e. Compensator Fa(Ω) can be simpler to implement
Upsampling effectively increases our sampling frequency, thus our ZOH pulse can be narrower and give us a better staircase approximation
This ‘smoother staircase’ will be easier to rectify with the compensator
  i.e. the transition bandwidth will be larger
In the frequency domain, we see the frequency axis compress by L; however, the analog frequencies upon recovery do not change!

## Slide 7: Downsampling
If we downsample by D, we keep every Dth sample (decimate the rest)
What happens in the frequency domain?
  Frequency response stretches by a factor of D
  Amplitude reduces by a factor of D (think conservation of energy)
Anti-aliasing filter prevents downsampling from aliasing our signal

## Slide 8: Fast Fourier Transform
Computational efficient implementation of the DFT
  Ordinary DFT requires N2 multiplies and N(N – 1) adds
  FFT requires only computations
Two main forms of FFT
  Decimation in Time
  Decimation in Frequency
We will consider the Radix 2 FFT, but other Radices may be used
Use Butterfly Structures to represent multiplies and adds

## Slide 9: Decimation in Time
Divide sequence into two groups
  Before we continue, remember that
We can form the first half of the DFT from these two sequences
And the second half…
Continually halve the sequences until you reach size 2

## Slide 10: Decimation in Frequency
Reverse of Decimation of Time
Compute points over entire DFT in even and odd groups
  DIT divides even and odd groups then computes points over smaller groups
Even k’s:
Odd k’s:

## Slide 11: Butterfly Structure Exercise
Draw the butterfly structure of a length 8 Decimation in Time FFT for xn

## Slide 12: Butterfly Structure Exercise
Draw the butterfly structure of a length 8 Decimation in Time FFT for xn

## Slide 13: Butterfly Structure Exercise
Decimation in Frequency is reverse of Decimation in Time

## Slide 14: Fast Linear Convolution
In order to obtain system response, we can multiply DFTs and take inverse DFT
  Be careful, this is not the same as convolution in time, but rather cyclic convolution in time
Therefore, in order to perform linear convolution from DFTs, we must first zero pad signals in order to make wrap-around terms go to zero
If xn has length N and hn has length M, then the resulting convolution is of length N+M – 1
  We must pad xn with M – 1 zeros
  hn with N – 1 zeros
This will allow multiplication of FFTs to produce linear convolution result from cyclic convolution
Note: we also typically do extra padding so that the signals are of power of 2 length to optimize the FFT

## Slide 15: References
Chapters 13 and 14 in Singer’s Textbook
Overlap Add and Overlap Save Stuff @ Chapter 14 Page 16+